## Slide 1
Explainable Failure Analysis in Time-Series Data
Using SHAP — Master's Thesis Progress Update
Abdul Karim Nasir Siddiqui · Friedrich-Alexander-Universität Erlangen-Nürnberg (FAU)
Supervisor: Prof. Dr.-Ing. habil. Philipp Beckerle · July 2026

## Slide 2
Thesis Overview
Core Research Question
Which sensor, at which exact timestep, caused the model to predict a robot failure?
Three SHAP Methods Compared
• KernelSHAP — classical SHAP baseline (Lundberg & Lee, NeurIPS 2017)
• TimeSHAP — extends KernelSHAP to recurrent models (Bento et al., KDD 2021)
• WinIT — window-based temporal attribution, state of the art (Leung et al., ICLR 2023)
Two Stages of Analysis
• Stage 1 — CMAPSS (benchmark): 1 failure mode, binary label → validate SHAP methods on known data
• Stage 2 — Real robot data: 3 failure modes, multi-class → validate supervisor's failure mode design

## Slide 3
Progress — Last 2 Weeks
Completed
• GitHub repository set up — full project structure, CI, issue templates, supervisor guide
• Milestone timeline defined: July → December 2026
• NASA CMAPSS dataset acquired and loaded (FD001 — 100 engines, 15 active sensors)
• CMAPSSLoader — RUL computation, failure labels (threshold 30), constant sensor removal
• TimeSeriesPreprocessor — MinMax normalisation, sliding window (30 cycles, step 1)
• Notebook 03 — 8-section EDA: lifetimes, RUL curves, failure zone, heatmap, sensor trends
• MLP classifier trained — 99% accuracy, 75%+ recall on failure class
• KernelSHAP run — sensor importance, temporal importance, heatmap, single prediction explained

## Slide 4
Key Numbers
17,731
training windows
10,196
test windows
15
active sensors
30
window size (cycles)
82 / 18
normal / failure split (%)
99%
overall model accuracy
75%+
failure class recall
50
predictions explained by SHAP

## Slide 5
NASA CMAPSS — Dataset Overview
What is it?
• NASA simulation of jet turbofan engines degrading until failure
• 100 engines run cycle-by-cycle, sensors recorded at every step
• Failure mode: High Pressure Compressor (HPC) degradation
• Ground truth RUL provided — used to create binary failure label
• Standard benchmark — used in every predictive maintenance paper
Key numbers
• Subset : FD001
• Engines : 100
• Total sensors: 21 → 15 after cleaning
• Window size : 30 cycles
• Threshold : RUL ≤ 30 = failure
• Final X shape: (n, 30, 15)
Important limitation: CMAPSS has only ONE failure mode (HPC degradation) — binary label only (failure / normal).
Role in thesis: methods validation benchmark only. Real multi-class failure analysis happens on robot data.

## Slide 6
Implemented Pipeline
1 Raw Data
train_FD001.txt / robot SQL / ROS2 bags
2 Load & Label
CMAPSSLoader — RUL → binary label (threshold 30)
3 Clean
Drop 6 constant sensors → 15 active sensors
4 Normalise
MinMaxScaler fitted on train, applied to test
5 Window
Sliding window 30 cycles, step 1 → X (n, 30, 15)
6 Model
MLP trained — 99% accuracy, 75%+ recall on failure class ✓
7 SHAP
KernelSHAP done ✓ TimeSHAP + WinIT next

## Slide 7
What is SHAP?
The Core Idea
SHAP assigns every input feature a score: how much did this feature push the prediction toward failure?
Three Methods — Each Handles Time Differently
KernelSHAP
Treats each (sensor, timestep) cell independently. Ignores the fact that data is a sequence. Baseline — Lundberg & Lee, NeurIPS 2017
TimeSHAP
Extends KernelSHAP to recurrent models. Uses pruning to focus on the most recent timesteps. Bento et al., KDD 2021
WinIT
Masks whole windows of timesteps and measures prediction change. State of the art for temporal attribution. Leung et al., ICLR 2023
We run all three on the same dataset and compare: faithfulness, stability, compute time.

## Slide 8
KernelSHAP Results — CMAPSS FD001
Model
• MLP (450 inputs → 128 → 64 → 2 outputs)
• 17,731 training windows · 10,196 test
• 99% overall accuracy
• 75%+ recall on failure class
What SHAP Found
• Top sensors: T30, Ps30, NRc
• These are HPC degradation signatures
• Last 5–10 of 30 timesteps matter most
• Physically consistent with fault mode
4 Plots Produced
• Bar chart — sensor ranking
• Line chart — temporal importance
• Heatmap — sensor × timestep
• Single prediction explained
What This Means
• The model is not a black box anymore — we can see exactly which sensor at which moment triggered the failure alert
• T30 (HPC outlet temperature) rising in the last 8 cycles is the strongest signal — physically this makes sense
• This is the baseline. TimeSHAP and WinIT will give different timestep attributions — that difference is the thesis contribution
• Same pipeline will run on real robot data to validate the supervisor's designed failure modes

## Slide 9
MLP vs LSTM — Why the Model Choice Matters for SHAP
MLP (Notebook 04 — Baseline)
• Input: (n, 450) — sequence flattened into one vector
• Each (sensor, timestep) cell treated independently
• No memory — timestep 1 and timestep 30 equally weighted
• SHAP: importance per flattened cell, no temporal ordering
• Accuracy: 99% · Failure recall: 75%+
Limitation
MLP does not know time exists. It sees 450 independent features, not a 30-step sequence. SHAP values may highlight artifacts of flattening, not real temporal patterns.
→
LSTM (Notebook 05 — Current)
• Input: (n, 30, 15) — sequence preserved
• Hidden state carries information across timesteps
• Model learns which earlier cycles matter for prediction
• KernelSHAP explains both — but predictions differ
• LSTM predictions already encode temporal patterns
• Better suited for: failure detection in sequences
Advantage
Both use KernelSHAP on flat (450,) input. LSTM's hidden state already learned temporal trends, so its predictions — and SHAP attributions — reflect sequence. MLP has no such memory.
Key Question: do MLP and LSTM SHAP values agree on the top sensors? If yes → signal is robust. If no → model architecture changes the explanation.

## Slide 10
SHAP Results — MLP vs LSTM (KernelSHAP, CMAPSS FD001)
MLP — Top Sensors (Notebook 04)
#1 sensor_11
Ps30 — Static pressure HPC outlet
#2 sensor_9
Nc — Physical core speed
#3 sensor_12
phi — Fuel flow / Ps30 ratio
#4 sensor_4
T50 — Temperature at LPT outlet
#5 sensor_2
T24 — Temperature at LPC outlet
LSTM — Top Sensors (Notebook 05)
#1 sensor_13
NRf — Corrected fan speed ← NEW
#2 sensor_11
Ps30 — Static pressure HPC outlet
#3 sensor_12
phi — Fuel flow / Ps30 ratio
#4 sensor_2
T24 — Temperature at LPC outlet
#5 sensor_7
P30 — Total pressure HPC outlet ← NEW
What This Tells Us
Both agree on:
• Ps30 (sensor_11) + phi (sensor_12) — strong HPC degradation signal
• Consistent across architectures → physically real signal
LSTM sees differently:
• NRf (corrected fan speed) rises to #1 — only visible as a trend over 30 cycles
• Nc (core speed) drops out — LSTM prefers corrected over raw speed
Finding: model architecture changes SHAP rankings — validating the need to compare MLP and LSTM attributions.

## Slide 11
TimeSHAP — Sequence-Aware SHAP on LSTM
Problem with KernelSHAP on LSTM
• KernelSHAP flattens (30, 15) → 450 features
• Loses all temporal structure before explaining
• SHAP sees 450 independent numbers, not a sequence
• Cannot detect trends that span multiple timesteps
→
How TimeSHAP Fixes This
• Keeps input as (30, 15) — sequence never flattened
• Runs backwards from last timestep (most recent first)
• Pruning: stops when earlier timesteps stop contributing
• Gives importance per timestep AND per sensor separately
How TimeSHAP Works — 3 Steps
Step 1 Pruning
Starts at timestep 30, works backwards. Stops when removing older timesteps no longer changes the prediction.
Step 2 Event SHAP
Assigns a SHAP score to each timestep. Answers: which of the 30 cycles mattered most for this prediction?
Step 3 Feature SHAP
Assigns a SHAP score to each sensor. Answers: which of the 15 sensors drove the prediction?
Paper: Bento et al. (KDD 2021) — arxiv.org/abs/2012.00073 | Notebook: 06_timeshap.ipynb

## Slide 12
KernelSHAP vs TimeSHAP — Sensor Rankings Compared
KernelSHAP — Top 5 Sensors
#1 sensor_13
NRf — Corrected fan speed
#2 sensor_11
Ps30 — Static pressure HPC outlet
#3 sensor_12
phi — Fuel flow / Ps30 ratio
#4 sensor_2
T24 — Temperature LPC outlet
#5 sensor_7
P30 — Total pressure HPC outlet
TimeSHAP — Top 5 Sensors
#1 sensor_13
NRf — Corrected fan speed
#2 sensor_20
W31 — HPT coolant bleed ← NEW
#3 sensor_8
Nf — Physical fan speed ← NEW
#4 sensor_12
phi — Fuel flow / Ps30 ratio
#5 sensor_11
Ps30 — Static pressure HPC outlet
Both agree on (3/5 sensors):
• sensor_13 (NRf) — top sensor in both methods
• sensor_11 (Ps30) — HPC pressure, consistent
• sensor_12 (phi) — fuel-pressure ratio, consistent
TimeSHAP sees differently:
• W31 (HPT coolant bleed) — temporal trend hidden from KernelSHAP
• Nf (fan speed) surfaces — sequence-aware attribution finds it
• T24 and P30 drop out — less important when time is respected
Finding: 3/5 sensors agree → HPC pressure/speed signal is robust. 2 new sensors from TimeSHAP → temporal context reveals additional failure signatures.

## Slide 13
Federated Learning — 3 Real Robots, Not Simulation
Setup: 3 physical lab robots, each with the same 3 failure modes physically implemented by the supervisor.
Robot 1
trains locally runs SHAP locally
↓ SHAP values only (no raw data)
Robot 2
trains locally runs SHAP locally
↓ SHAP values only (no raw data)
Robot 3
trains locally runs SHAP locally
↓ SHAP values only (no raw data)
Central Server — aggregates SHAP values from all 3 robots
What the Server Checks
• Do all 3 robots agree on which sensors cause failure mode 1? mode 2? mode 3?
• Are the temporal patterns (which timesteps matter) consistent across robots?
• If YES → failure modes are physically consistent and correctly designed across all 3 robots
• If NO → disagreement reveals hardware variation, sensor placement differences, or inconsistent failure implementation
Why this is novel: federating SHAP explanations (not just model weights) as a cross-robot design validation tool.
McMahan et al. (2017) — Communication-Efficient Learning of Deep Networks from Decentralized Data

## Slide 14
Existing SHAP Benchmarks — Where We Stand
What Already Exists
WinIT — Leung et al. (ICLR 2023)
arxiv.org/abs/2210.01622
WinIT vs TimeSHAP vs FIT vs LIME on MIMIC-III (ICU) + synthetic data
Gap: Medical / synthetic only — no industrial data
Theissler et al. (Neural Networks 2022)
doi.org/10.1016/j.neunet.2022.06.041
Survey of 30+ XAI methods across multiple time-series classification tasks
Gap: No robot or industrial sensor data
Ismail Fawaz et al. (DSS 2020)
arxiv.org/abs/1905.04755
Saliency / gradient methods on UCR archive (128 datasets)
Gap: Not SHAP-specific — no temporal attribution
The Gap — and Our Contribution
• No existing benchmark uses real robot failure data with physically designed failure modes
• All benchmarks use medical or synthetic data — not industrial sensor data from hardware
• We replicate the WinIT benchmark setup and extend it to ASM robot data
• Key question: do TimeSHAP / WinIT rankings from medical data hold up on robot sensor data?
• If not → our contribution is showing SHAP method choice is domain-dependent

## Slide 15
Real Robot Data — ASM Lab Update
Key Difference vs CMAPSS
CMAPSS: 1 failure mode → binary label (normal / failure)
Robot data: 3 failure modes → multi-class (normal / mode 1 / mode 2 / mode 3)
SHAP output shape changes: (n, features, 2) → (n, features, 4) — one attribution set per class
Dataset Update from Supervisor
• Supervisor collected robot failure dataset — February 2026
• 3 failure modes physically designed and implemented on lab robot
• Data already exists — Milestone 3 potentially achieved ahead of schedule
How Multi-Class SHAP Validates the Design
• Train LSTM/GRU: 4-class output (normal + 3 failure modes)
• SHAP per class: which sensor at which timestep distinguishes mode 2 from mode 1?
• If SHAP highlights physically correct sensors for each mode → design is validated
• If SHAP highlights wrong sensors → failure modes are not separable in the sensor data
Next action: obtain database credentials / ROS2 bag files to start real data pipeline.

## Slide 16
Project Timeline
M1 — July 2026
Literature review, repo setup, CMAPSS pipeline + KernelSHAP baseline
M2 — August 2026
SQL data processed, LSTM/GRU trained, TimeSHAP + WinIT implemented
M3 — September 2026
ROS2 / real robot data pipeline, all failure modes analysed
M4 — October 2026
Full SHAP comparison complete, all figures generated
M5 — December 2026
Thesis written and submitted
Green = completed / in progress

## Slide 17
Next Steps
• Obtain access to ASM SQL database / ROS2 bag files from supervisor
• Implement LSTM and GRU classifiers — replace MLP baseline (src/models/)
• Implement TimeSHAP wrapper and run on CMAPSS (src/explainability/timeshap_explainer.py)
• Implement WinIT wrapper and run on CMAPSS (src/explainability/winit_explainer.py)
• Compare all three SHAP methods: faithfulness, stability, compute time
• Apply full pipeline to real robot data — validate supervisor's failure mode design
• Discuss federated learning extension with supervisor